## Slide 1: APPLIED PHYSICS
Lecture 15
Nov. 06, 2023
Dr. Saif Ur Rehman

## Slide 2: What is a transistor?
A transistor is a 3 terminal electronic device made of semiconductor material.
Transistors have many uses, including amplification, switching, voltage regulation, and the modulation of signals

## Slide 3: Bipolar Transistor
A transistor is basically a Si or Ge crystal containing three separate regions.

## Slide 4: Architecture of BJTs
The bipolar junction transistor (BJT) is constructed with three doped semiconductor regions separated by two pn junctions
Regions are called emitter, base and collector

## Slide 5: Bipolar Transistor
The depletion layers do not have the same width, because different regions have different doping levels.

## Slide 6: Biasing
If both the junctions are forward biased free electrons enter the emitter and collector of the transistor, joins at the base and come out of the base.
If both the junction are reverse biased then small currents flows through both junctions only due to thermally produced minority carriers and surface leakage.

## Slide 7: Biasing
When the emitter junction is forward biased and collector junction is reverse biased then one expect large emitter current and small collector current but collector current is almost as large as emitter current.

## Slide 8: Transistor Current
The total current flowing into the transistor must be equal to the total current flowing out of it.

## Slide 9: Transistor Applications
Switching
Amplification
Variable Resistor
Impedance Matching
Voltage Regulation

## Slide 10: Basic circuits of BJT

## Slide 11: Operation of BJTs
BJT will operates in one of following four region
  Cutoff region (for digital circuit)
  Saturation region (for digital circuit)
  Linear (active) region (to be an amplifier)
  Breakdown region (always be a disaster)

## Slide 12: Operation of BJTs

## Slide 13: DC Analysis of BJTs
Transistor Currents:
IE = IC + IB
alpha (DC)
IC = DCIE
beta (DC)
IC = DCIB
  DC typically has a value between 20 and 200

## Slide 14: DC Analysis of BJTs
DC voltages for the biased transistor:
Collector voltage
VC = VCC - ICRC
Base voltage
VB = VE + VBE
  for silicon transistors, VBE = 0.7 V
  for germanium transistors, VBE = 0.3 V

## Slide 15: Q-point
The base current, IB, is established by the base bias
The point at which the base current curve intersects the dc load line is the quiescent or Q-point for the circuit

## Slide 16: Q-point

## Slide 17: DC Analysis of BJTs
The voltage divider biasing is widely used
Input resistance is:
RIN  DCRE
The base voltage is approximately:
VB  VCCR2/(R1+R2)

## Slide 18: End of Lecture-3
To download this lecture visit
http://imtiazhussainkalwar.weebly.com/