## Slide 1: Computer Organization & Assembly Language (CSC-205)
Lecture 15

## Slide 5: 5.3. STACK
What is a Stack?
  A Stack is a data structure following Last In, First Out (LIFO) principle
  Only the top element can be accessed for addition or removal
  Visual Example: Like a test tube of balls - only the top ball can be removed.
Key Stack Operations ?
  Push: Add an element to the top of the stack
  Pop: Remove the top element from the stack
  Peek (Read): You can look at elements inside, but can only remove from the top

## Slide 6: 5.3. STACK
Stack Behavior in Processors ?
  In 8088 processor, stack works with word-sized (2 bytes) data only
  The stack uses two registers:
    SP (Stack Pointer): Points to top of the stack
    SS (Stack Segment): Identifies stack's memory area
  Physical Address = SS:SP
Decrementing vs Incrementing Stack
  8088 uses a Decrementing Stack:
    Stack grows from higher to lower memory addresses
    SP is decremented by 2 on push
    SP is incremented by 2 on pop
  Example:
  Start at shelf 5 → next item in shelf 4 → then shelf 3
  *Other processors (like 8051) may use incrementing stacks

## Slide 7: 5.3. STACK
PUSH and POP Operations (Examples)
  Push Operation:
    SP = SP - 2
    [SP] = Operand (e.g. AX)
  POP Operation:
    Operand = [SP]
    SP = SP + 2
Example
  push ax pushes AX register onto stack
  pop ax retrieves it back

## Slide 8: 5.3. STACK
Importance of Stack
  Used to save and restore values (like register contents)
  Helps in:
    Subroutine calls (saving caller's registers)
    Program flow control (via CALL and RET)
CALL and RET Instructions
  CALL:
    Saves current Instruction Pointer (IP) on stack
    Loads new address in IP
  RET:
    Pops saved IP back to continue execution
    RET n: Additionally increments SP by n after return (used in parameter passing)

## Slide 9: 5.3. STACK
CALL and RET - Near and Far
  Near CALL/RET:
    Within the same segment
  Far CALL/RET (RETF):
    Across segments
    Pushes both Segment (CS) and Offset (IP) on stack
    RETF restores both
CAUTION with PUSH and POP
  The processor doesn't check logical correctness.
    push ax followed by pop dx is technically valid but may be logically wrong
  Ensure correct order:
    The order of POP must be the reverse of PUSH

## Slide 10: 5.3. STACK
Stack during Nested Subroutine Calls
  Stack can handle nested subroutines
  Each subroutine can:
    Push its own data and return address
    Use stack to manage data safely during complex calls

## Slide 11: 5.3. CALL and RET Example (Near CALL)
Scenario:
  Main program at IP = 3000 calls subroutine at 4000

## Slide 12: 5.3. CALL and RET Example (Near CALL)
During CALL:
  IP (3000) is pushed on stack
  SP becomes 1FFE
  IP becomes 4000

## Slide 13: 5.3. CALL and RET Example (Near CALL)
During RET:
  IP is popped from stack
  SP becomes 2000
  IP becomes 3000 (back to main program)

## Slide 14: Diagram 2: PUSH and POP Example
PUSH AX (AX = 017B):
  AX is pushed on stack
  SP becomes 1FFE

## Slide 15: Diagram 2: PUSH and POP Example
POP AX :
  AX is popped from stack
  SP becomes 2000

## Slide 16: Diagram 3: Nested CALL Example
Main Program → CALL Subroutine1 → Subroutine1 calls Subroutine2
  CALL Subroutine1:
    Push IP1 (Main address)
    SP = 1FFE
  In Subroutine1 → CALL Subroutine2:
    Push IP2 (Subroutine1 address)
    SP = 1FFC
  Make the diagram ?
  Also tell me :
  Output of RET from Subroutine2 ?
  Output of RET from Subroutine1 ?

## Slide 17: Diagram 3: Nested Call Example

## Slide 18: Diagram 3: Nested CALL Example
RET from Subroutine2:
    IP2 is popped
    SP becomes 1FFE
RET from Subroutine2:
    IP1 is popped
    SP becomes 2000

## Slide 19
End of Lecture